## Slide 1: Introduction to Operating Systems CS 1550
Spring 2022
Sherif Khattab
ksm73@pitt.edu
(Some slides are from Silberschatz, Galvin and Gagne ©2013)

## Slide 2: Announcements
Upcoming deadlines:
  Homework 11: due on 4/18
  Project 3: Late due date on 4/13
    Late penalty waived
  Lab 4: due on 4/15
  Quiz 3: due on 4/15
  Homework 12: due on 4/25
  Lab 5: due on 5/2
  Project 4 and Quiz 4: due on 5/2
  Bonus Homework: due on 5/2
  Course Post-Test: due on 5/2

## Slide 3: Muddiest Points (1/2)
when is the parity checked to see if there is a bit error
a little confused about parity example
How to flip the correct bits back that were changed with parity?
What is parity used for
ECC
What things move how using what in the disk
disk request time delay factors
  transfer time/rotating time/seek time
I feel like rotational delay and actual transfer time are overlapped. The sector is spending time to rotate to the head, and at the same time, the head is rotating to find that sector. Are they moving towards each other at the same time?

## Slide 4: Muddiest Points (2/2)
In the last top hat question, why the page table gets smaller if the page frames are larger. I understand that would mean less entries, but wouldn't each entry would be larger, making the overall table the same size?
What are RAIDs for?
Does RAID4 have any advantages over RAID5?
All of it, bro

## Slide 5: Problem of the Day – Part 1
How does a file system handle errors?
Answer: Defense in Depth
  multiple layers of error detection/correction

## Slide 6: When good disks go bad…
Disks have defects
  In 3M+ sectors, this isn’t surprising!
ECC helps with errors, but sometimes this isn’t enough
Disks keep spare sectors (normally unused) and remap bad sectors into these spares
  If there’s time, the whole track could be reordered…

## Slide 7: RAIDs, RAIDs, and more RAIDs
strip
strip
Stripe
RAID 0
(Redundant Array of Inexpensive Disks
RAID 1
(Mirrored copies)
RAID 4
(Striped with parity)
RAID 5
(Parity rotates through disks)

## Slide 8: Backing up a file system
A file system to be dumped
  Squares are directories, circles are files
  Shaded items, modified since last dump
  Each directory & file labeled by i-node number
File that has
not changed

## Slide 9: Bitmaps used in a file system dump

## Slide 10: Checking the file system for consistency
Consistent
Missing (“lost”) block
Duplicate block in free list
Duplicate block in two files

## Slide 11: Problem of the Day – Part 2
How does a file system hide disk access delays?
Answer: Caching

## Slide 12: File block cache data structures

## Slide 13: Log-structured file systems
Trends in disk & memory
  Faster CPUs
  Larger memories
Result
  More memory -> disk caches can also be larger
  Increasing number of read requests can come from cache
  Thus, most disk accesses will be writes
LFS structures entire disk as a log
  All writes initially buffered in memory
  Periodically write these to the end of the disk log
  When file opened, locate i-node, then find blocks
Issue: what happens when blocks are deleted?

## Slide 14: Log Structured File System

## Slide 15: Log Structured File System

## Slide 16: Disk block size
Dark line (left hand scale) gives data rate of a disk
Dotted line (right hand scale) gives disk space efficiency
All files 2KB
Block size

## Slide 17: Problem of the Day – Part 3
How do device drivers program I/O devices?
Answer: three methods
  polling
  Interrupts
  DMA

## Slide 18: How are I/O devices connected?
Single-bus
  All memory accesses go over a shared bus
  I/O and RAM accesses compete for bandwidth
Dual-bus
  RAM access over high-speed bus
  I/O access over lower-speed bus
  Less competition
  More hardware (more expensive…)
CPU
Memory
I/O
CPU
Memory
I/O
This port allows I/O devices access into memory

## Slide 19: Memory-Mapped vs. separate I/O Space
Separate I/O & memory space
0xFFF…
0
Memory
I/O ports
Memory-mapped I/O
Hybrid: both memory-mapped & separate spaces

## Slide 20: Example: Dynamic Frequency on XScale

## Slide 21: Programmed I/O example: printing a page
Printed page
ABCD EFGH
Kernel
User
A
Printed page
ABCD EFGH
ABCD EFGH
AB
Printed page
ABCD EFGH
ABCD EFGH

## Slide 22: Polling
copy_from_user (buffer, p, count); // copy into kernel buffer
for (j = 0; j < count; j++) { // loop for each char
while (*printer_status_reg != READY)
; // wait for printer to be ready
*printer_data_reg = p[j]; // output a single character
}
return_to_user();

## Slide 23: Hardware’s view of interrupts
Bus

## Slide 24: Interrupt-driven I/O
copy_from_user (buffer, p, count);
j = 0;
enable_interrupts();
while (*printer_status_reg != READY)
;
*printer_data_reg = p[0];
scheduler(); // and block user
if (count == 0) {
unblock_user();
} else {
j++;
*printer_data_reg = p[j];
count--;
}
acknowledge_interrupt();
return_from_interrupt();
Code run by system call
Code run at interrupt time
(Interrupt handler)

## Slide 25: What happens on an interrupt
Set up stack for interrupt service procedure
Ack interrupt controller, reenable interrupts
Copy registers from where saved
Run service procedure
(optional) Pick a new process to run next
Set up MMU context for process to run next
Load new process' registers
Start running the new process

## Slide 26: Direct Memory Access (DMA) operation

## Slide 27: DMA

## Slide 28: I/O using DMA
copy_from_user (buffer, p, count);
set_up_DMA_controller();
scheduler(); // and block user
acknowledge_interrupt();
unblock_user();
return_from_interrupt();
Code run by system call
Code run at interrupt time

## Slide 29: Disk drive structure
Data stored on surfaces
  Up to two surfaces per platter
  One or more platters per disk
Data in concentric tracks
  Tracks broken into sectors
    256B-1KB per sector
  Cylinder: corresponding tracks on all surfaces
Data read and written by heads
  Actuator moves heads
  Heads move in unison
sector
cylinder
platter
spindle
track
head
actuator
surfaces

## Slide 30: Disk scheduling algorithms
Schedule disk requests to minimize disk seek time
  Seek time increases as distance increases (though not linearly)
  Minimize seek distance -> minimize seek time
Disk seek algorithm examples assume a request queue & head position (disk has 200 cylinders)
  Queue = 100, 175, 51, 133, 8, 140, 73, 77
  Head position = 63
100
175
51
133
8
140
73
77
read/write head position
disk requests
(cylinder in which block resides)
Outside edge
Inside edge

## Slide 31: First-Come-First Served (FCFS)
Requests serviced in the order in which they arrived
  Easy to implement!
  May involve lots of unnecessary seek distance
Seek order = 100, 175, 51, 133, 8, 140, 73, 77
Seek distance = (100-63) + (175-100) + (175-51) + (133-51) + (133-8) + (140-8) + (140-73) + (77-73) = 646 cylinders
100
175
51
133
8
140
73
77
read/write head start

## Slide 32: Shortest Seek Time First (SSTF)
Service the request with the shortest seek time from the current head position
  Form of SJF scheduling
  May starve some requests
Seek order = 73, 77, 100, 133, 140, 175, 51, 8
Seek distance = 10 + 4 + 23 + 33 + 7 + 35 + 124 + 43 = 279 cylinders
100
175
51
133
8
140
73
77
read/write head start

## Slide 33: SCAN (elevator algorithm)
Disk arm starts at one end of the disk and moves towards the other end, servicing requests as it goes
  Reverses direction when it gets to end of the disk
  Also known as elevator algorithm
Seek order = 51, 8, 0 , 73, 77, 100, 133, 140, 175
Seek distance = 12 + 43 + 8 + 73 + 4 + 23 + 33 + 7 + 35 = 238 cyls
100
175
51
133
8
140
73
77
read/write head start

## Slide 34: C-SCAN
Identical to SCAN, except head returns to cylinder 0 when it reaches the end of the disk
  Treats cylinder list as a circular list that wraps around the disk
  Waiting time is more uniform for cylinders near the edge of the disk
Seek order = 73, 77, 100, 133, 140, 175, 199, 0, 8, 51
Distance = 10 + 4 + 23 + 33 + 7 + 35 + 24 + 199 + 8 + 43 = 386 cyls
100
175
51
133
8
140
73
77
read/write head start

## Slide 35: C-LOOK
Identical to C-SCAN, except head only travels as far as the last request in each direction
  Saves seek time from last sector to end of disk
Seek order = 73, 77, 100, 133, 140, 175, 8, 51
Distance = 10 + 4 + 23 + 33 + 7 + 35 + 167 + 43 = 322 cylinders
100
175
51
133
8
140
73
77
read/write head start