## Slide 1: Introduction to Operating Systems CS/COE 1550
Fall 2021
Sherif Khattab
ksm73@pitt.edu
(Some slides are from Silberschatz, Galvin and Gagne ©2013)

## Slide 2: Announcements
Upcoming deadlines:
  11/5: Homework 7 and Quiz 2
  11/8: Lab 3
  11/19: Project 3

## Slide 3: Last Lecture …
Memory sharing
  Fixed partitions
Memory protection
  Base and Limit registers

## Slide 4: Muddiest Points (Scheduling Algorithms)
Multi-level Feedback Queues
  Does a process in the lower queues of the multilevel feedback waste the extra time if it is not required max For example if a process has 2 time slots left to run but in that queue it runs for 4, what happens to the last 2 time slots?
  Multilevel feedback scheduler seems like a great solution, but how hard is it to implement?
Round robin
  Quantum versus time slice
  when using round robin how do you determine how long the time slice should we use to get most efficient ratio including context switch overhead
  What is the benefit of using a time slice
  when to switch in round robin
is priority scheduling preemptive?
SJF
  How are ties broken in SJF/SPN?
  When do we ever know the expected service time of a process?
  example of cpu burst estimation
  What are the important differences between preemptive and non-preemptive versions of shortest job first?
How is FCFS a fair scheduling algorithm?

## Slide 5: Muddiest Points (General CPU Scheduling)
Difference between dispatcher and scheduler? Also for studying purposes, will the final be cumulative?
Difference between non preemptive and preemptive
do you need preemption for there to be a time slice
are there any differences between preemptive and non-preemptive other than time slices?
the strengths and weaknesses of the scheduling techniques discussed so far
Honestly I’d like a table or easy to view breakdown of each method fro schedule. I feel we rushed through them

## Slide 6: Muddiest Points (Memory)
Within an embedded device, if the OS and any programs are stored in RAM, what happens if the device loses power?

## Slide 7: Today …
Paging and virtual memory
Page replacement algorithms

## Slide 8: Base and limit registers
Special CPU registers: base & limit
  Access to the registers limited to kernel (privileged) mode
  Registers contain
    Base: start of the process’s memory partition
    Limit: length of the process’s memory partition
Address generation
  Physical address: location in actual memory
  Logical address: location from the process’s point of view
  Physical address = base + logical address
  Logical address larger than limit => error
Process partition
OS
0
0xFFFF
Limit
Base
0x2000
0x9000
Logical address: 0x1204 Physical address: 0x1204+0x9000 = 0xa204

## Slide 9: Virtual memory
Basic idea: allow the OS to hand out more memory than exists on the system
Keep recently used stuff in physical memory
Move less recently used stuff to disk
Keep all of this hidden from processes
  Processes still see an address space from 0 – max address
  Movement of information to and from disk handled by the OS without process help
Virtual memory (VM) especially helpful in multiprogrammed system
  CPU schedules process B while process A waits for its memory to be retrieved from disk

## Slide 10: Virtual and physical addresses
Program uses virtual addresses
  Addresses local to the process
  Hardware translates virtual address to physical address
Translation done by the Memory Management Unit
  Usually on the same chip as the CPU
  Only physical addresses leave the CPU/MMU chip
Physical memory indexed by physical addresses
CPU chip
CPU
Memory
Disk controller
MMU
Virtual addresses from CPU to MMU
Physical addresses on bus, in memory

## Slide 11: Address Translation

## Slide 12: Paging and page tables
Virtual addresses mapped to physical addresses
  Unit of mapping is called a page
  All addresses in the same virtual page are in the same physical page
  Page table entry (PTE) contains translation for a single page
Table translates virtual page number to physical page number
  Not all virtual memory has a physical page
  Not every physical page need be used
Example:
  64 KB virtual memory
  32 KB physical memory
0–4K
4–8K
8–12K
12–16K
16–20K
20–24K
24–28K
28–32K
7
0–4K
4
4–8K
8–12K
12–16K
0
16–20K
20–24K
24–28K
3
28–32K
32–36K
36–40K
1
40–44K
5
44–48K
6
48–52K
-
52–56K
56–60K
-
60–64K
Virtual address space
Physical memory
-
-
-
-
-
-
-

## Slide 13: What’s in a page table entry?
Each entry in the page table contains
  Valid bit: set if this logical page number has a corresponding physical frame in memory
    If not valid, remainder of PTE is irrelevant
  Page frame number: page in physical memory
  Referenced bit: set if data on the page has been accessed
  Dirty (modified) bit :set if data on the page has been modified
  Protection information
Page frame number
V
R
D
Protection
Valid bit
Referenced bit
Dirty bit

## Slide 14: Implementing page tables in hardware
Page table resides in main (physical) memory
CPU uses special registers for paging
  Page table base register (PTBR) points to the page table
  Page table length register (PTLR) contains length of page table: restricts maximum legal logical address
Translating an address requires two memory accesses
  First access reads page table entry (PTE)
  Second access reads the data / instruction from memory
Reduce number of memory accesses
  Can’t avoid second access (we need the value from memory)
  Eliminate first access by keeping a hardware cache (called a translation lookaside buffer or TLB) of recently used page table entries

## Slide 15: Page replacement algorithms
Page fault forces a choice
  No room for new page (steady state)
  Which page must be removed to make room for an incoming page?
How is a page removed from physical memory?
  If the page is unmodified, simply overwrite it: a copy already exists on disk
  If the page has been modified, it must be written back to disk: prefer unmodified pages?
Better not to choose an often used page
  It’ll probably need to be brought back in soon

## Slide 16: Optimal page replacement algorithm
What’s the best we can possibly do?
  Assume perfect knowledge of the future
  Not realizable in practice (usually)
  Useful for comparison: if another algorithm is within 5% of optimal, not much more can be done…
Algorithm: replace the page that will be used furthest in the future
  Only works if we know the whole sequence!
  Can be approximated by running the program twice
    Once to generate the reference trace
    Once (or more) to apply the optimal algorithm
Nice, but not achievable in real systems!

## Slide 17: OPT Examples

## Slide 18: Not-recently-used (NRU) algorithm
Each page has reference bit and dirty bit
  Bits are set when page is referenced and/or modified
Pages are classified into four classes
  0: not referenced, not dirty
  1: not referenced, dirty
  2: referenced, not dirty
  3: referenced, dirty
Clear reference bit for all pages periodically
  Can’t clear dirty bit: needed to indicate which pages need to be flushed to disk
  Class 1 contains dirty pages where reference bit has been cleared
Algorithm: remove a page from the lowest non-empty class
  Select a page at random from that class
Easy to understand and implement
Performance adequate (though not optimal)

## Slide 19: NRU Operation